## Slide 1: How robots move – Navigation, Motion planning and Manipulation

## Slide 3: What is ROS
NOT an Operating System
Middleware
Set of libraries
Meta-operating system
Collection of software frameworks
Abstraction from hardware

## Slide 4: Why ROS?

## Slide 5: Usual approach
Write all the programs
Define a way of communicating between them
Write 3D simulation softwares
Implement all the robots

## Slide 6: What ROS offers
The middleware core
A set of libraries
Compatible 3D visualization and simulation tools
Open-source community support
Tools and libraries made for ROS – MoveIt, Gazebo
Additional services like rosbridge, and popular stacks

## Slide 7: Should YOU use ROS?
Overkill for small projects
Very Useful when the number of sensors and actuators increase
Essential when anything remotely complex is needed to be done
Perfect for robotics research
Good for prototyping but look for other options too

## Slide 8: ROS Versions
http://wiki.ros.org/Distributions

## Slide 9: Let’s shift to ROS irl

## Slide 10: Let’s get those things in order first

## Slide 11: What you need to think about
How do you describe where is a robot?
  How do you represent a body in space?
  How many parameters you’ll need to have to represent a robot?
How does the robot know where it has to go?
How does the robot plan its motion – the path it will take, the speed it will go ahead with, etc.
How will the robot do what it is supposed to do?

## Slide 12: Words you’ll often hear - common robotics terminology
Degrees of Freedom
End effector
Payload
Actuator
Joint
Link
Constraint
Modeling

## Slide 13
How Many joints and links are there?

## Slide 15: Problem 1 – Where is my robot
Configuration
Configuration Space
Degrees of Freedom

## Slide 16: Configuration
A specification of the position of all points of a robot (cartesian coordinate, cylindrical, spherical, articulated)
How many parameters you would need to describe a body in space? (We only talk about rigid bodies)

## Slide 17: Configuration space (C-Space)
The space of all configurations
C-Spaces have topologies – plane, sphere, torus, cylinder
Two types of representation for curved configuration spaces – implicit representation and explicit parametrization (minimum number of coordinates)
Implicit representation is much more popular – rotation matrices, no time derivatives, just a surface embedded in a higher-dimensional space

## Slide 18: Degrees of freedom
Minimum number of numbers you need to represent a configuration
Rigid bodies in 3D have 6 DOF
The general formula for calculating DOF:
And there is GrÜbler’s formula

## Slide 19: Problem 2 – Going from one point to another

## Slide 20: lEtS uSe aI

## Slide 22
F1
F2

## Slide 23
Transformation Matrix
Why 0s and 1?

## Slide 24: Principle movements
Rotations
Rotation along X axis
Rotation along Y axis
Rotation along Z axis
Translations
Translation along X axis
Translation along Y axis
Translation along Z axis

## Slide 25: The rotations

## Slide 26: The Translations

## Slide 27: Translation matrices

## Slide 28
F1
F2
Every possible movement is a combination
What’s the transformation matrix?

## Slide 29: Three things that can be done using transformation matrices:
Represent a configuration
Change reference frame
Displace a vector or frame

## Slide 30: Overview of ROS

## Slide 31: Problem 3 – How does the robot plan its movement?
Motion Planning

## Slide 32: Why motion planning?

## Slide 33: Why motion planning?
There might be obstacles in the environment
Higher degree of freedom = Larger number of approaches to reach the same goal position
Not every approach has the same energy requirements
There might be design or operation constraints

## Slide 34: Going back to Configuration Space
C-Space: C = C(free) + C(obstacles)
Obstacles = set of points in the C Space

## Slide 35: Types of path planning algorithms
Trajectories and paths
Fully actuated and underactuated
Offline and real time
Exact and approximate

## Slide 36: Properties of Motion Planning algorithms
Computational complexity
Multiple query vs single query
Completeness
  Resolution completeness (discretization)
  Probabilistic completeness (planning times -> infinity => probability finding a solution -> 100%)

## Slide 37: Popular path planning algorithms
DFS and BFS
Dijkastra’s Algorithm
A* Algorithm
Optimization of these (Lifelong A*, D*, variations of Anytime algorithms)

## Slide 38: Trees and Graphs
Motion planning is often done in discretized manner
There are nodes and edges
More often than not weighted
directed graphs are used
Trees are used with sampling based methods

## Slide 39: A* Algorithm
Graph search algorithm
https://clementmihailescu.github.io/Pathfinding-Visualizer/

## Slide 40: Grid Methods
Dividing the C-Space into grids
Not very efficient
Optimizations done in 3D
Resolution complete

## Slide 41: Sampling based methods
Probabilistic methods
Tree-based
Popular approaches –
  Probabilistic Roadmap (PRM)
  Rapidly Exploring Random Tree (RRT) and RRT*

## Slide 42: Virtual Potential Fields
Robots supposed to be attracted or repulsed by an artificial potential field

## Slide 43: Optimization and newer developments
Non-linear optimization
Saptiotemporal LSTM Nets based learning algorithms

## Slide 44: How does the robot do what it is supposed to?
Manipulation

## Slide 45: Robotic Manipulation
Changing the state of an environment to a desired one

## Slide 46: Simulation of Manipulation
Not trivial
Must incorporate feedback control and perception
Must replicate the environment to the max
https://colab.research.google.com/github/RussTedrake/manipulation/blob/master/intro.ipynb#scrollTo=C1sdq2R88C16
https://colab.research.google.com/github/RussTedrake/manipulation/blob/master/intro.ipynb#scrollTo=4cTkwpJU8tGX

## Slide 47: Thank You